## Slide 1
Prototype Electric Vehicle
Presented to
Dr. Ahmed Lotfy

## Slide 2
Team Members
Abd-Elrahman
Ali
Emad
Mohamed
Ragab
Awab
Ezz-Eldien
Magdi
Ehab
Ashraf

## Slide 3
Agenda Items
Project Objective
Progress overview (H/S)
Introduction
BLDC Motor
Hardware Design
Hardware Testing
Open loop system
Closed loop system
Timeline

## Slide 4
Project Objective
Building BLDC Inverter from scratch
Improving system efficiency
Perform regenerative
breaking
Design and implement BMS

## Slide 5
Our Progress
This will be achieved by:
Hardware
Software

## Slide 6
Hardware
From Here (one Leg)
To There
(3phase open loop inverter)

## Slide 7
STM32 specs.

## Slide 8
(three phase inverter)
Software

## Slide 9
Introduction
Why Brushless Motor ?
DC Motor
Pros
High starting torque
Low cost
Suited to Industrial Environment
Cons
High Maintenance Cost
Lower Speed
Brushless Motor
Pros
Long Lifespan
High Efficiency
Low noise and quiet operation
Cons
Require Controller
Cost Of Controller and Drivers

## Slide 10
Introduction
Why BLDC ?

## Slide 11
BLDC motors structure
We can consider BLDC motors as a flipped version of brushed DC motors as we have :
Permanent magnet represents the rotor
3 phase coils represents the stator
We can consider that BLDC motors and PMSM motors are synchronous motors but they have differences in EMF ch/cs which lead to different control algorithms.

## Slide 12
Principle of Operation
Inner working of the motor
We will use simple configuration where the rotor only consists of a single pole pair and the stator consists of three coils spaced at
Applying voltage across two phases A and C generates a combined magnetic field along
the dashed line

## Slide 13
The rotor now starts to rotate to align itself with the stator magnetic field
There are six possible ways of energizing coil pairs
What this mean if we can commutate the correct phases every ?
We can make the motor spin and this is called six step commutation or trapezoidal control
Principle of Operation
Inner working of the motor

## Slide 14
Principle of Operation
Inner working of the motor

## Slide 15
The motor creates zero torque
Maximum torque occurs when the fields are at to each other
Principle of Operation
Inner working of the motor

## Slide 16
IN BLDC WE USE AN ELECTRONIC CONTROLLER FOR THIS PURPOSE A SENSOR DETERMINE THE POSITION AND SPEED OF THE ROTOR AND BASED ON THIS INFORMATION THE CONTROLLER DECIDES WHICH COILS TO ENERGIZE
Principle of Operation
Which and when each coil is Energized ?

## Slide 17
Hardware Design
Component Selection of the inverter circuit

## Slide 18
18
Hardware Design
PCB Design
1 – old Version
20

## Slide 19
19
19
19
Hardware Design
PCB Design
2 – Updated Version

## Slide 20
20
20
20
Hardware Design
PCB Design
3 – Current Version

## Slide 21
21
21
21
21
Hardware Testing
Inverter Output
Inverter circuit output line voltage with
Inductive load without Snubber Circuit
[R = 35 Ω, L = 1.5 mH].

## Slide 22
22
22
22
22
Hardware Testing
Snubber Design

## Slide 23
23
23
23
23
23
Hardware Testing
Results after Snubber
Inverter circuit output line voltage with Inductive
load with Snubber Circuit
[R = 35Ω, L = 1.5 mH].

## Slide 24
24
24
24
24
24
Hardware Testing
Testing Inverter with Motor

## Slide 25
Open loop model
In this MATLAB model we try to simulate motor performance at several operating conditions
We will go through into each block to explain it

## Slide 26
Six step commutation​
Hall sensors is used to detect the rotor position in order to commutate the correct phases to keep rotor spinning based on this lookup table

## Slide 27
We implemented this logic in MATLAB simulink environment ​
1
1
1
0
0
0
1
1
1
1
1
1

## Slide 28
Open loop Speed control
We can use gate pulses generated based on six step commutation to control the speed of the motor by applying any PWM techniques
In our model we use method based on triangular wave form compared with reference voltage

## Slide 29
In our model we used non complementary switching method which means that PWM can be applied on gate pulses of high side MOSFETS
Gate pulses with Duty cycle = 50%

## Slide 30
Back EMF wave form

## Slide 31
Inverter output voltage
Expected line voltage

## Slide 32
Inverter output voltage
Line voltage
Diode Freewheeling
VDC
Back EMF

## Slide 33
Diode freewheeling
During the commutation , each switch becomes off after 120 electrical degrees a current flowback through the body diode in switch until the energy stored in phase winding disappears , after that the terminal voltage becomes equal to the back-EMF voltage

## Slide 34
Torque ripples

## Slide 35
Torque ripples
The gross output torque from BLDC motors is the sum of beneficial electromagnetic torque (steady torque) and unwanted torque or torque ripple produced by :
Commutation
DC bus ripple
Commutation /electromagnetic torque ripple in BLDC motors
If we assume an ideal square-current waveform applied to the winding, the torque generated will be constant without any ripple
In reality , winding currents cannot rise or fall instantaneously because of the winding inductance.
This causes torque ripple during the commutation of BLDC motor phase currents as shown in Figure 1
Figure 1

## Slide 36
The following figures show three different cases depending on the current’s rising and falling rate of the commutating windings
Case A : the current increase and decrease rates of the two windings are the same as shown in Figure
Case B : there is a mismatch in the current’s rising and falling rate of the commutating windings, which in turn causes commutation torque ripple

## Slide 37
Torque ripple due to DC-bus voltage ripple
Bulk electrolytic capacitors are used on the high-voltage DC bus link of a mains-operated BLDC
The value of the capacitor for a given load decides the magnitude of ripple on the DC bus
A simple way to minimize torque ripple caused by DC-bus voltage ripple is to use a very-high-value DC bus capacitor this will increase overall size and system cost, as high-voltage capacitors are bulkier and take up a significant share of the bill of materials cost. A general thumb rule is to calculate the DC bus capacitor value to maintain DC-bus voltage ripple within 5-10%, depending on the quality of performance required.
With DC bus compensation
Without DC bus compensation

## Slide 38
Motor performance

## Slide 39
Phase current

## Slide 40
Open loop full duty
Open loop variable duty

## Slide 41
speed control of the BLDC motor

## Slide 42
Speed calculation
The six steps represents 360o electrical of the motor rotation
The number of motor pole pairs  p = 20
The six steps represents = 18o mech.
The rotor will rotate = 3o mech. per sector (step).
The motor speed = = (rpm)
The time between two steps is obtained by XOR the three hall sensors signals then measuring the time between two changes using input capture unit in the micro controller.

## Slide 43
= = 3.33msec

## Slide 44
The implementation of speed measurement code

## Slide 45
PI speed controller and limiter
PI speed control of the BLDC motor
The speed of the motor is compared with its reference value and the speed error is processed in proportional- integral (PI) speed controller.
The output of this controller is considered as the reference torque.
e(t) = ωref − ωm
Where
and, are the gains of PI speed controller.
T is the sampling time.

## Slide 46
Vs
2
2
2
Transfer function model
At any sector
Mathematical model for BLDC motor
How to determine ?

## Slide 47
Transfer function
Assume
Poles = -1000 , -3.97
To simplify, we can neglect the pole at -1000. So it will become a first order system

## Slide 48
Inverter Gain
+
Inverter
It is valid to assume it as a DC gain
??

## Slide 49
Choose way lower than as we consider the inverter as a DC gain.
Make low-frequency gain very large
To minimize steady-state error
Make cross-over frequency as high as possible
To maximize closed-loop bandwidth.
For the system to response to wider range of frequencies.
Maintain large enough phase margin
Phase margin > 0 is required for stability.
Larger phase margin is required for well behaved closed-loop response.
Choose way higher than to maximize closed-loop bandwidth.
Choose
Controller Design Requirements
Choose
Step input, Type 0 system

## Slide 50
Proportional (P) Compensator
Is high at low frequency
Proportional Integral (PI) Compensator

## Slide 51
Step Reference
Step Response of (P)
Steady State Value
Steady State Error
Settling time
Steady State Value
Steady State Error
Settling time
Step Response of (PI)

## Slide 52
Testing on Simulink Motor Model

## Slide 53
Step input (Reference)
At fixed load
Speed performance
Solution:
Using PI controller with Anti-Windup
Windup problem

## Slide 54
Current limiter
The magnitude of the three phase current ( ) is determined by using the reference torque ( )
A limit is put on the speed controller output depending on permissible maximum winding currents.
From the E.Bike inverter nameplate:
Operating Power = 330Watt
Operating voltage = 36-48vDC
For 3-phase inverter ( conduction mode)  Vrms(line) = Vdc * = 25.5 : 44 volt
 = 10 amp

## Slide 55
IV. Reference current generator
The reference currents for each phase , are function of the value of reference current magnitude and the rotor position.
Sector | Rotor position | Active switches |  |  | 
1 | 0 - 60 | S1 , S6 |  | - | 0
2 | 60 - 120 | S1 , S2 |  | 0 | -
3 | 120 - 180 | S3 , S2 | 0 |  | -
4 | 180 - 240 | S3 , S4 | - |  | 0
5 | 240 - 300 | S5 , S4 | - | 0 | 
6 | 300 - 360 | S5 , S6 | 0 | - | 
Sector | Rotor position | Active switches |  |  | 
1 | 0 - 60 | S1 , S6 |  |  | 0
2 | 60 - 120 | S1 , S2 |  | 0 | 
3 | 120 - 180 | S3 , S2 | 0 |  | 
4 | 180 - 240 | S3 , S4 |  |  | 0
5 | 240 - 300 | S5 , S4 |  | 0 | 
6 | 300 - 360 | S5 , S6 | 0 |  | 
Reference current w.r.t rotor positions look up table

## Slide 56
Reference current generator in simulink

## Slide 57
Back Emf ‘s and currents
Ia_ref formation

## Slide 58
Current control
Approach_1 : Hysteresis current control (discrete (ON/OFF) mode)
Approach_2 : PI current control (continuous (analog) mode)
Empirical guide lines for tuning , :

## Slide 61
 | Hysteresis current control | PI current control
Design | Easy, no | Require calculations of
Control action | The controller produces a discontinuous ON/OFF signal | The controller emits an analog output signal, so it need PWM module.
Switching frequency | Undefined so, it is difficult to design a filter to suppress switching harmonics | Easy to design a filter
 | Hysteresis current control | PI current control
Design |  | 
Control action | The controller produces a discontinuous ON/OFF signal | The controller emits an analog output signal, so it need PWM module.
Switching frequency | Undefined so, it is difficult to design a filter to suppress switching harmonics | 
Comparison between Hysteresis & PI current control
Hysteresis control is preferable

## Slide 62
Comparison of BLDC drives with and without Hysteresis Current Controller

## Slide 63
speed control of the BLDC motor in simulink

## Slide 64
Speed Performance at different load torques and at different reference speeds
At different load torques
The motor dynamic behavior is analyzed when different load torques is applied at time t = 2s for the same speed (150 rpm).
Curve | Load torque (N.m) | Speed fall%
C1 | 2 | 2.7
C2 | 3.5 | 6
C3 | 5 | 9.3
C1
C3
C2

## Slide 65
Speed Performance at different load torques and at different reference speeds
At different reference speed
The motor dynamic behavior is analyzed when same load torque (1N.m) is applied.
Curve | Speed (rpm) | Settling time (sec)
C1 | 50 | 0.75
C2 | 100 | 0.8
C3 | 150 | 0.9
C2
C1
C3

## Slide 66
15
Timeline
Aug - Oct
Oct - Nov
Brainstorming
Idea Pitching
Nov - Dec
Research
June - July
Testing - Documentation
Jan - May
Implementation

## Slide 67
Draft

## Slide 68
is per-phase inductance
is per-phase resistance
is L-L voltage constant
Transfer function
Assume

## Slide 69
Parameter | Value
Armature per-phase resistance, | 
Armature per-phase inductance, | 
Back emf constant, (L-L) | 
Torque constant, | 
Viscous friction coefficient, | 
Rotor moment of inertia, | Rotor radius : Wheel radius: Motor weight: Wheel weight:
No. of poles, | 
No. of phases, | 
Rated DC voltage | 
Rated power, | 
Parameter | Value
Motor Parameters

## Slide 70
Assume Load Torque

## Slide 72
Inner loop
outer loop
Controller Design Requirements
Frequency of inner and outer loop should be away from of inverter.
Inner loop should response faster than outer loop.

## Slide 74
Current PI controller
For
By adding an integrator (pole at origin), and a real zero at -1000

## Slide 75
Speed PI controller
For
By adding an integrator (pole at origin), and a real zero at -6.38